## Slide 1
Blue Halo Clearance Algorithm
Seismic Bracing Proactive Space Reservation
FEMA E-74 · ASCE/SEI 7-10 §13.6 · EN 1998-1 + DIN EN 1998-1/NA · NFPA 13 · SMACNA
BH-001 · LOD 300 → 350 space reservation · Pluggable jurisdiction configs · BCF 2.1 output
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5

## Slide 2
The problem in the design cycle
Space for supports is designed after the space is gone
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
LOD 300 — services routed
Pipes, ducts and conduit are modelled to their own envelope. The support system does not exist yet, so nothing reserves room for it.
LOD 350 — supports designed
Hangers and sway braces are added. They need a diagonal leg and a base footprint that the surrounding services have already occupied.
Result — rework, not clash
The clash is real but late. Rerouting a duct run at LOD 350 costs an order of magnitude more than shifting a pipe at LOD 300, and it lands on the programme.
Blue Halo — reserve first
Compute the support envelope at LOD 300 and publish it as a reserved volume. The conflict surfaces while services are still cheap to move.

## Slide 3
How the clearance envelope is derived
Jurisdiction-driven, not hard-coded
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
halo_bbox = element_bbox ⊕ effective_clearance
⊕ is a uniform expansion on every face. effective_clearance is read from the jurisdiction config, never from code.
effective_clearance = base_clearance + seismic_zone_addition + hospital_addition
The shipped SB-001 config sets a 200 mm base: authored screening calibration, not a code value. No code or guide held gives a braced-service clearance.
The implementation applies a uniform buffer because that is what the corpus can support. Angle-aware wedge envelopes for diagonal cable and rod bracing are deferred: the corpus carries no brace geometry to validate them against, and an unvalidated wedge would be a guess wearing a formula.

## Slide 4
Four-phase architecture
Each phase fails independently and reports why
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Phase
Function
Input
Output
1
Geometry normalisation
Any IFC representation type
World-coordinate bounding boxes, mm
2
Halo generation
Element bbox + jurisdiction rule
Expanded clearance envelope per element
3
Spatial indexing
All candidate geometries
Uniform grid, cell-bucketed
4
Collision detection
Halo + indexed candidates
ClashReport per intersection, severity banded
Separation matters for diagnosis: a model that yields no halos has failed Phase 1, and the run says so rather than reporting zero conflicts as a clean result.
Measured on the corpus: Phase 1 resolved geometry for 49,736 of 49,736 MEP elements — 100%.

## Slide 5
Phase 1 — geometry normalisation
The phase that decides whether anything else can run
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Why it is not trivial
Real exports overwhelmingly use IfcMappedItem and IfcFacetedBrep. A fast vertex reader handling only tessellated sets, polylines and swept solids resolves none of them — measured at 0 of 87 elements on the AISC steel models.
What the harness does
Evaluates real geometry through ifcopenshell.geom's multithreaded iterator, which handles every representation type, then converts to axis-aligned boxes in millimetres.
Two settings that decide correctness
use-world-coords must be set, or every element returns in local coordinates near the origin and everything appears to clash. The iterator emits SI metres regardless of declared file units, so results scale by 1000.
Verified against a fixture whose true extents are known exactly, so the unit handling is checked rather than assumed.

## Slide 6
Phase 2 — halo generation
Deterministic, and traceable to its config rule
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Read the rule, not a constant
The brace variant selects a ClearanceRule from the loaded jurisdiction config. Base clearance, spacing and angle limits all come from the pack.
Expand uniformly
The element bounding box grows by the effective clearance on every face, producing an axis-aligned envelope in millimetres.
Record what produced it
Each HaloVolume carries the rule variant, the clearance applied and the flags that modified it, so a volume can be traced back to the config rule and its provenance status.
Immutable with respect to source
The original element geometry is never mutated; the halo is a separate object keyed by GlobalId.

## Slide 7
Phase 3 — spatial indexing
Why brute-force pairing does not finish
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
brute force O(n²) → uniform grid ≈ O(n) for spatially sparse models
West Riverside mechanical alone carries 8,732 duct and pipe segments: 76 million pair tests without pre-filtering.
Cell sizing
Cell edge is the median element extent, floored at four times the clearance, so a halo touches few cells.
Bucketing
Every candidate bbox is inserted into each cell it overlaps; a halo queries only its own cells.
Exactness preserved
Results are identical to brute-force pairing. Only the comparisons that could not intersect are removed.
This is the difference between a sweep that completes in an hour and one that does not complete.

## Slide 8
Phase 4 — collision detection and severity
AABB intersection, banded by overlap fraction
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
overlap_ratio = overlap_volume ÷ halo_volume
Band
Threshold
Measured across corpus
Share
Critical
ratio ≥ 0.25
5,236
2.34%
Major
ratio ≥ 0.05
6,699
3.00%
Minor
ratio < 0.05
211,581
94.66%
The banding is a spatial heuristic, not a standards-derived threshold — stated as such in Appendix B under threats to validity. Table B.6 shows how sensitive the totals are to the clearance input, which is the stronger reason to treat severity as triage rather than verdict.

## Slide 9
Hospital MEP corridor — brace family comparison
One element, three candidate supports, one clearance regime
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Brace family
Clearance
Halo volume (mm³)
Conflicts
Recommendation
Angle iron — fire
200 mm
688,500,000
1
Marginal
Angle iron — mechanical
200 mm
688,500,000
1
Marginal
Rod
200 mm
688,500,000
1
Marginal
Cable
200 mm
688,500,000
1
Preferred on footprint
All four brace-type variants in the SB-001 config share one authored clearance; no source held distinguishes them. That is a gap in the config, not a property of the building. Where a config does differentiate, the comparison separates and the smallest-footprint family wins.
This is the honest form of the comparison: the method distinguishes families; the SB-001 config does not yet let it.

## Slide 10
Standards sensitivity — the counter-intuitive result
Raising the clearance requirement raises findings and lowers severity
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Clearance
Jurisdiction
Clashes
Critical
vs 200 mm
25 mm
—
30,332
148
0.29×
100 mm
—
69,307
38
0.67×
200 mm
SB-001 authored calibration¹
104,144
31
1.00×
457.2 mm
—
172,812
16
1.66×
600 mm
—
212,870
11
2.04×
¹ BIMGUARD SB-001 screening calibration (authored thresholds, not code values)
Raising the clearance from the 200 mm row to the 457.2 mm row yields 66% more clashes but 48% fewer Critical ones. Severity is an overlap ratio against halo volume, so a larger clearance inflates the denominator faster than the numerator.
The finding is an argument that the severity heuristic needs rethinking, not retuning. It held on two independent model subsets, at 1.62× and 1.66×.

## Slide 11
Validation dataset
What the algorithm was run against
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
37 / 38
models processed 8 repositories
49,736
MEP elements 100% geometry
223,516
clashes detected across the corpus
37 / 37
BCF archives valid
Corpus and controls
Hospitals, offices, industrial plant and mixed-use, IFC2x3 and IFC4, from Revit, ArchiCAD and Autodesk toolchains. Two same-building schema twins act as controls: rows 9/14 differ by 0.00% and rows 8/13 by 0.11%, so the result does not depend on the export schema.

## Slide 12
Validation results — tests and integrity
Every archive parsed, not merely counted
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
11 / 11
Blue Halo harness checks passed
8 / 8
end-to-end IFC pipeline checks
44 / 44
HTTP route tests (4 known-gap xfail)
100%
geometry resolution 49,736 elements
What BCF validity means here
All 37 archives were opened and every XML part parsed: bcf.version and project.bcfp present, one complete topic folder per clash carrying markup.bcf, viewpoint.bcfv and snapshot.png, zero malformed XML. Counting entries would not have established this.

## Slide 13
Performance measured across the corpus
Where the time actually goes
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Stage
Measured
Complexity
Note
Full sweep, 37 models
3,594 s
—
Download, parse, halo, clash, engines, BCF
Mean per model
≈ 97 s
—
Geometry evaluation dominates
Largest model
632 s
—
NBU_MedicalClinic, 207 MB, 5,952 MEP
Geometry evaluation
8–95 s per model
O(n)
ifcopenshell.geom multithreaded iterator
Clash detection
sub-second to seconds
≈ O(n)
Uniform grid; O(n²) without it
Smallest MEP model
4.8 s
—
wbdg office, 31 piping elements
Per-model timings are recorded in validation_sweep_summary.json and reproduce on re-run from cache.

## Slide 14
Academic contribution
What Blue Halo adds
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Proactive rather than reactive
Reserving support space at LOD 300 inverts the usual order, in which the support system discovers that its space is already gone.
Jurisdiction as data
Clearance, spacing and angle limits are loaded from versioned JSON configs, so a new standard is a data addition rather than a code change.
Measured at corpus scale
100% geometry resolution over 49,736 elements across two IFC schemas and three toolchains, with schema twins as controls.
A quantified sensitivity result
The clearance-severity inversion is a reproducible finding about the metric itself, not about any one building.

## Slide 15
Limitations
Stated plainly
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Axis-aligned boxes overstate intersection
A clash is an AABB overlap. Diagonal and non-convex members are over-approximated, so counts are an upper bound, not a defect list.
Uniform buffer, not a brace-shaped envelope
Real sway braces are diagonal members with a base plate. The wedge envelope is deferred until brace geometry exists to validate against.
Severity is a spatial heuristic
Overlap fraction of halo volume, not a standards-derived threshold. Table B.6 shows its sensitivity to the clearance input.
One clearance regime per run
The SB-001 config assigns every brace variant the same authored clearance, so variant comparison is degenerate under it.

## Slide 16
Post-FMP roadmap
R1 – R5, with the dependency each carries
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Ref
Enhancement
Dependency
Target
R1
Angle-aware wedge envelope for diagonal bracing
Brace geometry in the corpus to validate against
Q1 2027
R2
Non-circular and rectangular halo profiles
Profile data per brace family
Q1 2027
R3
Cable sag modelling (catenary)
Span and pretension inputs
Q2 2027
R4
Severity model grounded in standards
Clause basis for a non-ratio metric
Q2 2027
R5
Seismic zone auto-population from site data
Hazard map lookup and IFC round-trip
Q3 2027
R4 is the item the sensitivity result argues for most directly.

## Slide 17
Standards compliance
What each source supplies
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Standard
Supplies
Applied in
EN 1998-1:2004+A1:2013
§4.3.5 (non-structural elements)
Gives no MEP brace spacing or clearance
DIN EN 1998-1/NA:2018-10
German NA; DIN 4149 withdrawn
Gives no MEP brace spacing or clearance
FEMA E-74 (4th ed., December 2012)
A guide, not a code
Duct area threshold, importance factors
ASCE/SEI 7-10 §13.6
What FEMA E-74 defers to
Upstream reference; not held
SMACNA / MSS SP-58
Sway bracing and hanger support practice
Brace family footprints
ISO 16739-1 / BCF 2.1
IFC schema and issue exchange
Input parsing and topic output
There is one SB-001 config, not a jurisdictional pair. Neither EN 1998-1 nor the German National Annex dimensions MEP bracing; DIN 4149:2005-04 was withdrawn and replaced by DIN EN 1998-1:2010-12 with its National Annex; it is historical only.

## Slide 18
Jurisdiction as data, not as code
How a new standard enters the system
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
BIMGUARD SB-001 is a screening tool whose dimensional thresholds are authored calibration except where marked sourced, and it is not a substitute for design to ASCE/SEI 7-10 §13.6 or EN 1998-1.
Every threshold carries a provenance block with a status: 3 sourced, 2 derived, 9 authored. FEMA E-74 (4th ed., December 2012) evidences the duct area threshold and the importance factors, and gives upstream brace spacing maxima that the authored calibration is deliberately tighter than. The remaining thresholds are authored, with no source held.
Adding a jurisdiction is a data change with a provenance record, not a code change.

## Slide 19
Integration into the compliance pipeline
Where Blue Halo sits
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Input
Normalised IFC geometry and property sets, plus the jurisdiction clearance config selected for the project.
Output
One BCF 2.1 topic per breach, carrying both GlobalIds, overlap volume, severity band and the clearance rule that produced the envelope.
Model write-back
Pset_HaloReservation on the braced element: brace type, rule variant, clearance applied, element and halo bounding boxes.
Status
Breaches present hold the container at S2. Resolution is either a service move or an accepted LOD 350 reservation recorded against the element.

## Slide 20
BCF output — what a reviewer receives
Enough to act without opening the tool
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Field
Content
Source
Topic title
Brace type and source element class
HaloVolume.brace_type
Description
Both GlobalIds, overlap volume in mm³, ratio
ClashReport.description
Priority
Critical / Major / Minor
Severity band
Due date
2, 7 or 21 days by severity
Banding table
Viewpoint
Camera and component selection on the clash
viewpoint.bcfv
Labels
blue_halo, seismic_bracing, brace type
Topic labels
37 of 37 archives validated: every part well-formed, every topic folder complete.

## Slide 21
Comparison to current practice
The same conflict, found at two different prices
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Reactive — today
Model services at LOD 300. Design supports at LOD 350. Run clash detection. Discover the support has no room. Reroute services that are already coordinated, re-issue, re-review.
Proactive — Blue Halo
Model services at LOD 300. Compute the support envelope from the jurisdiction rule. Publish it as a reserved volume. Conflicts surface while services are still cheap to move.
What changes
Not the conflict — the timing. The same geometric fact is surfaced one design stage earlier, before the coordination effort that makes it expensive to undo.
The corpus cannot price this: cost avoidance depends on project commercials the models do not carry. What it does establish is that the detection works at scale.

## Slide 22
RQ2 — the spatial component answered
Can proactive reservation work on real federated models?
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
YES
demonstrated across 37 models
100%
geometry resolution no fallback needed
0.00% / 0.11%
schema twin deltas
223,516
clashes detected and exported
What the evidence supports
Halo generation and clash detection are deterministic, schema-independent and scale to the largest models in the corpus. What the corpus cannot yet support is brace-family differentiation, because the SB-001 config does not distinguish clearance by hardware. The method is validated; that particular comparison is not.

## Slide 23
Key findings
What the corpus established
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Geometry is not the obstacle
100% resolution across both IFC schemas and three authoring toolchains, using the full geometry iterator rather than a vertex shortcut.
The result is schema-independent
Same-building twins in IFC2x3 and IFC4 produced identical and near-identical clash counts — 0.00% and 0.11% apart.
Clearance choice dominates the outcome
A 2× clearance change moves total clashes by 2× and Critical count in the opposite direction. The clearance value is the most consequential input.
Severity needs a standards basis
Overlap ratio is defensible as triage and indefensible as a verdict. R4 addresses it.

## Slide 24
Blue Halo Clearance Algorithm
Questions?
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5