## Slide 1
BIMGUARD AI
Galvanic Corrosion Compliance Module
Automated BIM Compliance Checking Using LLM-Translated Engineering Rules
Group 5 | Masters in BIM Management | Zigurat Global Institute of Technology | 2026

## Slide 2
THE PROBLEM
Galvanic Corrosion Is Invisible in Standard BIM Workflows
⚠
Invisible Risk
Standard BIM clash detection finds geometric overlaps — not electrochemical incompatibility. Dissimilar metal pairings pass undetected.
💸
Financial Impact
Global corrosion costs exceed USD 2.5 trillion annually. MEP fixings and supports are among the highest-frequency premature failure categories.
📋
No Audit Trail
Current practice relies on individual engineer knowledge. There is no systematic record of material compatibility decisions for ISO 19650 or Golden Thread compliance.
Every year, incompatible material pairings specified at design stage reach construction unchallenged.

## Slide 3
TECHNICAL BACKGROUND
Galvanic Corrosion: The Science
What causes it:
Two dissimilar metals in electrical contact
A common electrolyte (moisture, water, salt spray)
A potential difference between the metals drives ion flow
The anodic (more active) metal corrodes; the cathodic metal is protected
The three drivers BIMGUARD AI measures:
Voltage Gap
EMF potential difference between metals (V)
Area Ratio
Anode-to-cathode surface area ratio
Environment
Electrolyte conductivity & chloride level
Galvanic Series (extract)
CATHODIC (protected)
Gold / Titanium
SS 316 (passive)
SS 304 (passive)
Copper / Brass
Carbon Steel
Galvanised Steel
Aluminium alloys
Zinc / Magnesium
ANODIC (corrodes)
↓

## Slide 4
BIMGUARD AI SOLUTION
How BIMGUARD AI Checks Galvanic Corrosion
1
IFC Model Input
Read material assignments & spatial data via IfcOpenShell
2
Classify Environment
Map IFC space type tags to one of 7 environment classes
3
Score Each Pairing
Voltage gap + area ratio + environment → composite 0–1 score
4
PREN Check
Verify stainless grade meets minimum PREN for environment
5
Output Results
BCF issues + IFC Pset_CorrosionRisk + Asset Register
Every check is explainable, auditable, and traceable to a named standard — BIMGUARD AI's White Box Architecture.

## Slide 5
RISK SCORING
Composite Risk Score — How It Works
Composite Score = (0.50 × Voltage Risk) + (0.30 × Area Ratio Risk) + (0.20 × Environment Multiplier)
50%
Voltage Risk
Actual gap vs. NASA-STD-6012 threshold for the environment tier
30%
Area Ratio Risk
Small anode on large cathode amplifies corrosion current density
20%
Environment Mult.
Electrolyte conductivity & chloride level multiplier (0.2–1.5)
Risk bands:
LOW
< 0.35
Log in asset register — no immediate action
MEDIUM
0.35 – 0.65
Flag — specify isolation detail on drawing
HIGH
0.65 – 0.85
BLOCK — BCF issue; lead engineer to resolve
CRITICAL
> 0.85
BLOCK — compliance failure; redesign mandatory

## Slide 6
HIGH-RISK SCENARIOS
Top MEP Material Pairings: Risk at a Glance
Anodic Material
Cathodic Material
Environment
Voltage Gap
Risk
Aluminium facade panel
SS 316 fixing
Coastal
0.72V
CRITICAL
Copper pipework
Galvanised hanger
Plant room
0.55V
MEDIUM
Carbon steel beam
SS 316 bracket
Urban ext.
0.52V
HIGH
SS 304 fixings
SS 304 fixings
Pool env.
0.0V*
HIGH
Cast iron drainage
Copper pipe
Interior
0.45V
MEDIUM
Galvanised purlin
SS 316 roof fixing
Coastal
0.67V
HIGH
Lead flashing
Aluminium frame
Exterior
0.35V
MEDIUM
Copper roof pipe
Aluminium sheet
Coastal
0.60V
CRITICAL
Carbon steel base plate
SS 316 anchor bolt
Industrial
0.52V
HIGH
Aluminium cable tray
Carbon steel bracket
Interior
0.20V
LOW
* SS 304 in pool environment fails PREN adequacy check (PREN 18 < required 26) — not a voltage gap failure.

## Slide 7
ENVIRONMENT CLASSES
Why Environment Matters: The Conductivity Multiplier
Seawater is ~700× more conductive than rainwater. The same material pairing carries fundamentally different risk in a coastal splash zone versus a dry interior.
Interior Dry
×0.2
Interior Conditioned
×0.3
Urban Exterior
×0.6
Industrial
×0.8
Swimming Pool
×1.1
Coastal
×1.2
Marine Splash
×1.5
NASA-STD-6012
Voltage Thresholds
Controlled (interior)
≤ 0.50 V
Normal (urban exterior)
≤ 0.25 V
Harsh (coastal / pool)
≤ 0.15 V

## Slide 8
PREN ADEQUACY
The Grade Selection Failure Mode Clash Detection Cannot Find
A correctly paired stainless specification can still fail if the grade is inadequate for the environment. BIMGUARD AI checks PREN independently of voltage gap.
PREN = %Cr + 3.3 × %Mo + 16 × %N
Source: IMOA Design Manual for Structural Stainless Steel, 4th Ed.
PREN
18
SS 304
PREN
24
SS 316
PREN
35
Duplex 2205
PREN
42
Super Duplex 2507
Minimum PREN by Environment
Interior dry
10+
Urban exterior
18+
Industrial
22+
Pool / Coastal
24–26+
Marine splash
40+

## Slide 9
BIM INTEGRATION
BIMGUARD AI Outputs: BCF Issues + IFC Property Sets
BCF Issue Output
Title: [BIMGUARD-GC] CRITICAL — Aluminium / SS_316
Priority: Critical | Status: Active
Assigned To: Design Lead + Client Rep
Due Date: 3 days from check date
Voltage gap: 0.72V (threshold: 0.15V)
Environment: coastal | Score: 0.96
Action: BLOCK — redesign mandatory
Mitigation: Isolation sleeve + washer required
IFC GUID: [component identifier]
Labels: GalvanicCorrosion | Risk-Critical | coastal
Pset_CorrosionRisk (IFC)
CorrosionRiskFlag: Critical
GalvanicPairMaterialA: Aluminum_alloy_6063
GalvanicPairMaterialB: SS_316_passive
VoltageGap_V: 0.72
AreaRatioAnodeCathode: 0.0024
EnvironmentClass: coastal
CompositeRiskScore: 0.96
MitigationRequired: Redesign
MitigationStatus: Outstanding
FirstInspectionYear: 1
BIMGUARDRulesetVersion: GC-001 v1.0
BCFIssueGUID: [linked BCF topic GUID]

## Slide 10
HANDOVER & ASSET MANAGEMENT
From Design Check to O&M Manual: The Asset Register
BIMGUARD AI generates a Corrosion Asset Register at handover — the initialisation data set for the building's 25-year corrosion management programme.
Component ID
Materials
Environment
Risk
Mitigation
Inspect Year
FM Action
GC-001
Al / SS316
Coastal
CRIT
Redesign
Year 1
Design Lead
GC-002
Cu / Galv.
Plant Rm
MED
Iso. washer
Year 5
M&E Eng.
GC-003
CS / SS316
Urban Ext
HIGH
Iso. washer
Year 3
Str. Eng.
GC-004
SS304 / SS304
Pool
HIGH*
Upgrade grade
Year 2
M&E Eng.
GC-005
CI / Cu
Interior
MED
Di. union
Year 5
FM Team
Building Safety Act 2022 — Golden Thread:
The Pset_CorrosionRisk IFC property set, linked to BCF issue GUIDs, constitutes a continuously maintainable Golden Thread record of corrosion safety decisions for higher-risk buildings.

## Slide 11
CLIENT READINESS
20 Client Questions — BIMGUARD AI Has the Answer
High-Risk Scenarios (8 questions)
"We found corroding brackets — how do we know this won't happen again?"
"Which fixings are at risk in our coastal facade?"
"The pool plant room is failing — what's causing it?"
"Can we mix stainless and aluminium on the roof?"
Design & Specification (7 questions)
"Which stainless grade do I specify for this location?"
"Do I need isolation washers on every fixing?"
"How far apart on the galvanic series is 'safe'?"
"Can you check our whole model for this?"
Compliance & Liability (5 questions)
"What standard governs this?"
"Who is liable if a specification causes galvanic failure?"
"What goes in the O&M manual for corrosion?"
"How does this meet the Golden Thread requirement?"
BIMGUARD AI generates citable, standards-referenced answers to all 20 question categories from BIM model data.

## Slide 12
VALIDATION
Engine Validation: 5/5 Scenarios Correctly Classified
001
SS fixing through aluminium facade — coastal
Expected: CRITICAL
Actual: 0.96 → CRITICAL
✓
002
Copper pipe on galvanised bracket — plant room
Expected: MEDIUM
Actual: 0.54 → MEDIUM
✓
003
Carbon steel beam with SS bracket — urban exterior
Expected: HIGH
Actual: 0.73 → HIGH
✓
004
SS 304 fixings in pool — PREN adequacy check
Expected: PREN FAIL
Actual: PREN 18 < 26 → FAIL
✓
005
Cast iron to copper drainage — dry interior
Expected: MEDIUM
Actual: 0.48 → MEDIUM
✓

## Slide 13
CONCLUSIONS
What BIMGUARD AI Delivers
🔍
Automated Detection
Every material pairing in the model checked — not just the ones the engineer happens to notice.
📐
Standards-Referenced
NASA-STD-6012, IMOA PREN thresholds, ISO 19650 IFC output — fully auditable White Box decisions.
📄
BCF + IFC Output
Issues route directly to the right engineer with priority, due date, and mitigation recommendation.
🏗
Handover Ready
Corrosion Asset Register generated at practical completion for O&M manual and Golden Thread compliance.
Next Steps: Crevice corrosion extension | Probabilistic environment classifier | buildingSMART Pset submission | Live project pilot

## Slide 14
REFERENCES
Key References
NASA-STD-6012 (2016)
Corrosion Control for Aerospace Applications — voltage threshold framework
WorldStainless / Euro Inox (2025)
Stainless Steel in Contact with Other Metallic Materials — corrosion rate data & compatibility matrices
IMOA (2020)
Design Manual for Structural Stainless Steel, 4th Ed. — PREN values & environment selection
Prosoco Tech Note 104 (2021)
Galvanic Corrosion in Mechanical Anchors — area ratio analysis & construction applications
AUCSC Basic Corrosion Course (2024)
Comprehensive galvanic series, electrolyte conductivity & corrosion cell physics
Aslam et al., PMC (2024)
XGBoost / DNN corrosion prediction in industrial cooling water pipelines
npj Materials Degradation (2025)
AI-driven corrosion prediction in marine engineering
Taylor & Francis (2025)
AI Applications in BIM — Systematic Mapping Study across 10 BIM dimensions
De Gruyter (2026)
Deep Learning in Corrosion Assessment — CNN, RNN, GAN approaches
Farinha et al. (2019)
BIM-based corrosion under insulation prediction — doi: 10.1016/j.autcon.2019.102985