## Slide 1
Architectural Code Analysis
Building Envelope and Spatial Compliance — Specification and Design
IBC · ADA · EN 17210 · ASTM E814 · NFPA 272 · UL 1479
AR-001 – AR-006 · Designed ruleset · Not implemented — post-FMP scope
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5

## Slide 2
Status of this work
What is designed, and what is not built
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
The ruleset is specified
Six rules, each with its query path through the IFC schema, its threshold basis in a cited code, and its output contract. That specification is the contribution presented here.
The engine is not implemented
No ARCH module exists in the codebase. A search for AR-001 through AR-006 returns nothing, and no architectural rule appears in the compliance runner or the engine registry.
No accuracy figure is claimed
Precision, recall and per-rule accuracy would require an implementation and a labelled corpus. Neither exists, so no such figure appears in this deck.
Why it is presented anyway
The design demonstrates that the method generalises beyond corrosion, and it is the concrete scope for the next phase. Presenting a specification as a specification costs nothing; presenting it as a result would.

## Slide 3
Scope of architectural analysis
Four families of check
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Fire rating continuity
Whether a compartment boundary actually holds: wall and slab ratings, and the sealing rating of everything that passes through them.
Egress verification
Travel distance to exit, door width and swing direction, dead-end limits, exit count against occupancy.
Accessible routes
Clear width, running slope and cross-slope along circulation paths; turning and approach space at fixtures.
Spatial adjacency
Whether incompatible uses are separated by the rating their combination demands.

## Slide 4
The six designed rules
Each with a query path and a threshold basis
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Ref
Rule
Primary IFC query
Threshold basis
AR-001
Fire rating continuity
Pset_WallCommon.FireRating
IBC compartmentation
AR-002
Accessible route geometry
Circulation IfcSpace boundaries
ADA / EN 17210
AR-003
Egress path verification
IfcDoor + IfcSpace topology
IBC travel distance
AR-004
Penetration sealing
IfcOpeningElement + seal Pset
ASTM E814 / NFPA 272
AR-005
Barrier-free space
IfcSpace geometry, fixture clearance
ADA clear floor area
AR-006
Spatial adjacency separation
IfcRelSpaceBoundary
IBC use separation
Every rule resolves to a query the IFC schema can answer and a threshold a code clause supplies. That is the test a rule must pass to enter the set.

## Slide 5
AR-001 — fire rating continuity
The check that compartmentation actually holds
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Query
All IfcWall and IfcSlab carrying Pset_WallCommon.FireRating or the slab equivalent; then every IfcOpeningElement that passes through them.
Evaluate
For each penetration, compare the sealing system rating against the rating of the element it breaches. A 2-hour wall with a 1-hour sleeve is a 1-hour wall.
Output
Critical where seal rating is below element rating; Approved where equal or greater; data-quality issue where either rating is absent — which, on the corrosion corpus, was the common case.
Why it matters
This is the failure mode that is invisible in geometry and fatal in service. The model is clash-free and the compartment does not hold.

## Slide 6
AR-003 — egress path verification
Geometry that determines whether people get out
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Step
Operation
Reference
1
Identify exits: IfcDoor with exit classification
IBC Ch. 10
2
Build space topology from IfcRelSpaceBoundary
ISO 16739-1
3
Compute travel distance from the farthest occupied point
IBC common path
4
Compare against occupancy-dependent maximum
IBC travel distance table
5
Check door clear width and swing direction
IBC 1010, ADA 404
6
Verify exit count against occupant load
IBC 1006
Steps 1–4 are the ones that need real graph traversal rather than property lookup, and they are where the implementation effort concentrates.

## Slide 7
AR-002 — accessible route geometry
Dimensional compliance along circulation
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Dimension
Requirement
Standard
Clear width, unobstructed
≥ 915 mm (36 in)
ADA 403.5 / EN 17210
Running slope
≤ 1:20 (5%) without ramp provisions
ADA 403.3
Cross slope
≤ 1:48 (2%)
ADA 403.3
Passing space interval
≤ 61 m (200 ft)
ADA 403.5.3
Changes in level
≤ 6 mm without bevel
ADA 303
Width is measured at intervals along the path rather than once, because the binding constraint is usually a local pinch point — a column, a door leaf, a radiator — not the nominal corridor width.

## Slide 8
AR-004 — penetration sealing
Matching the seal to what it breaches
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Through-element
Minimum seal rating
Standard
Duct through rated wall
Equal to wall rating
ASTM E814 / NFPA 272
Pipe through rated slab
Equal to slab rating
ASTM E814 / NFPA 272
Conduit through rated barrier
Equal to barrier rating
UL 1479 / ASTM E814
Cable tray through rated wall
Equal to wall rating, F and T rated
UL 1479
This is the rule with the clearest cross-discipline dependency: the penetrating element belongs to MEP, the barrier to architecture, and the seal to neither package until someone owns it. A federated check is the only place it can be caught.

## Slide 9
AR-005 and AR-006
Barrier-free space and use separation
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
AR-005 — barrier-free space
Turning circle 1525 mm diameter or T-turn equivalent. Forward approach 760 mm wide by 1220 mm deep; side approach 1220 by 760. Knee clearance 685 mm high, 280 mm deep. Counter height 865 mm maximum at accessible positions.
AR-006 — spatial adjacency
Mechanical plant above a threshold input against residential occupancy: 1-hour minimum. Hazardous storage against occupancy: 2-hour. Exit stair enclosure against electrical switchroom: 1-hour. Evaluated by walking IfcRelSpaceBoundary and reading the separating element's rating.

## Slide 10
How the rules would read the model
Inputs the IFC must actually carry
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Rule
Required input
Availability in the corrosion corpus
AR-001
FireRating on walls and slabs
Rarely populated
AR-002
Circulation space geometry
Present where IfcSpace is modelled
AR-003
Door classification and space topology
Partially present
AR-004
Penetration seal Pset
Effectively absent
AR-005
Fixture and clear-space geometry
Present where modelled
AR-006
Space use classification
Partially present
The corrosion sweep already measured what federated models carry, and the pattern generalises: geometry is reliably present, semantic property data is not. AR-001 and AR-004 would face the same input-availability wall that MM-001 and XM-001 hit.

## Slide 11
What validation would require
The work that has not been done
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
An implementation
Six comparator modules, each loading a versioned ruleset and emitting the standard Issue contract, wired into the engine registry.
A labelled corpus
Models where the correct answer is known independently — from an approved building-control submission, not from the tool itself. Without that, precision and recall have no referent.
A method for spatial ground truth
Egress distance and accessible width need a measured baseline. Corrosion could lean on material tables; geometry compliance cannot.
Honest reporting of coverage
The corrosion work showed that a 100% flag rate can mean zero input coverage. Any ARCH result must report coverage alongside findings from the first run.

## Slide 12
Design case 1 — isolation ward penetration
Worked through the specification, not executed
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
2 hr
barrier rating IBC compartment
600 mm
oval duct penetration
2 hr
sleeve F-rating ASTM E814
PASS
AR-004 as specified
What the rule would conclude
Seal rating equals barrier rating, so the compartment holds and the penetration is compliant. The value of the check is not this case but its inverse: a 1-hour sleeve in the same opening produces a clash-free, geometrically valid model that fails compartmentation, and nothing in current tooling would say so.

## Slide 13
Design case 2 — single-exit floor plate
Where the rule earns its cost
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
75 × 45 m
floor plate footprint
118 m
travel distance farthest corner
76 m
IBC maximum common path
FAIL
AR-003 as specified
Why the timing matters more than the finding
A 42 m overrun is not a detail to resolve in coordination; it requires a second stair core, which is structure, foundations and floor plate. Found at LOD 300 it is a design revision. Found at construction it is a redesign. The rule is cheap; the stage at which it runs is what makes it valuable.

## Slide 14
Integration with the existing pipeline
How ARCH would fit what already runs
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Same Issue contract
ARCH rules would emit the mechanism-agnostic Issue used by every corrosion engine, so the reporter, BCF exporter and asset register need no change.
Same engine registry
Registration alongside GC-001, CC-001 and MC-001, so a run reports ARCH availability and coverage in the same status table.
Cross-discipline by construction
AR-004 reads MEP penetrations against architectural barriers — a check neither package can perform alone.
Same honesty requirement
Coverage reported beside findings from the first run, so an ARCH flag rate is never read without the input availability that produced it.

## Slide 15
Academic contribution of the specification
What the design establishes
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
The method generalises
The pattern — versioned ruleset, IFC query path, cited threshold, mechanism-agnostic Issue — transfers from corrosion to code compliance without modification.
Cross-discipline checking has a home
Penetration sealing belongs to no single package. A federated rule engine is the natural place for it, and AR-004 shows the shape.
Input availability is predictable
The corrosion corpus already measured what federated models carry. ARCH can predict its own coverage problem before implementation.
Scope is bounded and costed
Six rules, each with a defined query and threshold, is a specification a successor can implement against.

## Slide 16
Limitations of the design
Known before a line is written
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Prescriptive, not performance-based
AR-004 compares ratings. It cannot evaluate an equivalent assembly that achieves the same performance by other means, which is how much real fire engineering is argued.
Planar geometry assumptions
Egress and accessible-route logic assumes floor-plan traversal. Split levels, ramps and mezzanines need vertical routing that the design does not yet cover.
Dependent on absent property data
AR-001 and AR-004 need ratings that the corrosion corpus showed are rarely populated. Implementation without a data strategy would reproduce the MM-001 outcome.
Code scope is jurisdictional
IBC and ADA thresholds are US. EN 17210 differs. The jurisdiction-config pattern from Blue Halo would need to carry across.

## Slide 17
Post-FMP roadmap
R1 – R6 for the architectural engine
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Ref
Enhancement
Prerequisite
Target
R1
Implement AR-001 and AR-004 (fire and sealing)
Ruleset packs in the shipped schema
Q1 2027
R2
Implement AR-003 egress with space-graph traversal
Space topology extraction
Q2 2027
R3
Implement AR-002 and AR-005 accessibility
Circulation geometry extraction
Q2 2027
R4
Labelled validation corpus
Models with approved control submissions
Q2 2027
R5
Jurisdiction configs (IBC / EN 17210)
Standards research per Blue Halo pattern
Q3 2027
R6
Performance-based equivalence for AR-004
Assembly performance data
Q3 2027
R4 is the gating item: without a labelled corpus, R1–R3 can be implemented but not validated, and the deck would face the same evidence problem it avoids today.

## Slide 18
Standards referenced
Sources for each threshold
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Standard
Supplies
Rules
IBC — International Building Code
Compartmentation, travel distance, exit count
AR-001, AR-003, AR-006
ADA — Americans with Disabilities Act
Route width, slope, clear space
AR-002, AR-005
EN 17210
European accessibility equivalents
AR-002, AR-005
ASTM E814 / NFPA 272
Penetration firestop test method
AR-004
UL 1479
Through-penetration firestop systems
AR-004
ISO 16739-1
IFC schema, spatial relationships
All
Each would be carried in a versioned pack rather than embedded in code, matching the corrosion and Blue Halo pattern.

## Slide 19
Designed output contract
What an ARCH finding would carry
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Field
Content
Why it is required
rule_id
AR-001 … AR-006
Identifies the rule that fired
element_id
IFC GlobalId of the failing element
Anchors the finding to the model
band
Critical / High / Medium / Low
Triage order for the reviewer
citations
Standard and clause governing the requirement
Makes the finding arguable on evidence
metadata
Measured value against required value
Shows the margin, not just the verdict
mechanism
fire_rating, egress, accessibility …
Keeps distinct failures separately actionable
This is the existing Issue contract, unchanged. ARCH rules would populate the same structure the corrosion engines already use, which is why the reporter, BCF exporter and asset register need no modification to carry them.

## Slide 20
Regulatory context
Why an auditable trail matters here
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Building Safety Act 2022
Requires demonstrable, auditable evidence that compliance was considered — not merely asserted at hand-over.
Pset write-back
An ARCH finding would attach to the element, so the compliance state travels with the object through federation and hand-over.
BCF as the review record
Each finding becomes a topic with a viewpoint, so the reviewer sees what the rule saw.
ISO 19650 status codes
S2 while unresolved, S4 with an NCR raised, Status A on acceptance — the same lifecycle the corrosion engines already use.

## Slide 21
Cross-discipline integration
Where ARCH and the corrosion engines meet
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
ARCH reads MEP
AR-004 evaluates MEP penetrations against architectural barriers. Neither discipline's model contains both halves.
MEP reads ARCH
Corrosion environment class is inferred from architectural spatial containment — space name, storey, zone.
Findings stay separate
One Issue per mechanism, because the mitigations differ. A firestop sleeve does not fix a galvanic couple.
The dependency already runs in one direction today: environment classification reads architectural spatial data. AR-004 would close the loop.

## Slide 22
Honest summary
What may and may not be claimed
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
6
rules fully specified
0
rules implemented
0
accuracy figures claimed
R1–R6
roadmap with prerequisites
The claim this deck makes
That the compliance method demonstrated on corrosion extends to architectural code checking, and that the extension has been specified to the level of query path and cited threshold. It does not claim the engine exists, that any model has been checked, or that any accuracy has been measured. Those claims would need R1 and R4 first.

## Slide 23
Key points
What to take from this specification
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Code compliance is machine-checkable in principle
Every one of the six rules resolves to an IFC query and a cited threshold. None requires judgement the schema cannot supply.
Fire and egress carry the life-safety weight
AR-001, AR-003 and AR-004 are the rules whose failure modes are fatal rather than costly, and they are first on the roadmap.
Input availability will be the binding constraint
The corrosion corpus already showed it. ARCH should measure coverage from its first run rather than discover it later.
The architecture is already in place
Issue contract, engine registry, BCF exporter and Pset write-back all exist and are engine-agnostic.

## Slide 24
Architectural Code Analysis
Questions?
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5