## Slide 1
Galvanic Corrosion Engine
Detecting Material Incompatibility in MEP Building Services
NASA-STD-6012 · WorldStainless · IMOA Design Manual · AUCSC 2024
GC-001 · 22-material electrochemical series · 7 environment classes · PREN adequacy
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5

## Slide 2
Why galvanic corrosion matters
A predictable, preventable failure mode that no BIM tool checks
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
The electrochemical process
Two dissimilar metals in electrical contact, bridged by an electrolyte, form a cell. The less noble metal becomes the anode and corrodes preferentially. Rate scales with the potential gap between them and with the cathode-to-anode area ratio.
Real-world consequences
Perforation of the anodic member, typically at the joint, long before design life. Field remediation runs 6–10× the cost of the design-stage specification change that would have prevented it, and arrives with programme delay attached.
The standard gap
Clash detection resolves geometry, not chemistry. Two touching elements of incompatible material are a valid clash-free model. No mainstream BIM tool interrogates material pairing at the joint.
GC-001 asks the question the geometry cannot: given what these two elements are made of, and where they sit, will one consume the other?

## Slide 3
Three research questions
The academic scope that frames this engine
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
RQ1 — Detection from existing IFC data
Can corrosion risk in MEP building services be reliably identified from the material, spatial and zone metadata already present in an IFC model at LOD 300, without additional modelling effort?
RQ2 — Dual-mechanism simultaneous checking
Can galvanic and crevice corrosion be evaluated in the same pass, such that each reports the failures the other cannot see, rather than collapsing into one combined score?
RQ3 — OpenBIM cross-platform deployment
Can a compliance checker operating purely on IFC input and BCF output work across authoring tools without vendor plugins or proprietary APIs?

## Slide 4
The 22-material electrochemical series
Ordered noble to active; the gap between any pair drives the risk
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Material
Potential (mV SCE)
PREN
Environment suitability
Platinum
+250
—
Inert; laboratory service only
Titanium Gr 2
−100
—
All classes including E7 coastal
SS316 / 1.4401
−50
25.2
E1–E4; marginal above E5
SS304 / 1.4301
−80
18.6
E1–E2 only; pits in chloride
Copper C12200
−350
—
E1–E4; avoid coupling to steel
Bronze / gunmetal
−400
—
E1–E4 valve bodies
Carbon steel
−600
—
E1–E2 dry only; coat otherwise
Galvanised steel
−980
—
Sacrificial; reverses above 60 °C
Zinc
−1030
—
Anode material, not a service metal
Magnesium
−1600
—
Sacrificial anode only
Full series holds 22 entries. Risk rises with separation: copper against carbon steel is a 250 mV gap; copper against galvanised steel is 630 mV.

## Slide 5
Seven environment classes
Each multiplies the base electrochemical risk
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Class
Name
Description
Multiplier
Example location
E1
Controlled indoor
Conditioned, RH < 45%
0.8×
Office ceiling void
E2
Heated indoor
Conditioned, RH 45–60%
1.0×
Riser cupboard
E3
Humid indoor
Intermittent condensation
1.2×
Plant room, laundry
E4
Outdoor sheltered
No direct rain, ambient RH
1.4×
Covered walkway
E5
Outdoor exposed
Direct wetting, UV
1.6×
Roof plant
E6
Coastal
Airborne chloride < 5 km
1.7×
Seafront plant deck
E7
High-corrosivity
Process chemical, pool hall
1.8×
Pool plant, dosing room
Class is inferred from IFC spatial containment — space name, storey and zone — and recorded on the finding so the inference is auditable.

## Slide 6
PREN: Pitting Resistance Equivalent Number
Whether a stainless grade suits the environment it sits in
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
PREN = %Cr + 3.3 × %Mo + 16 × %N
IMOA Design Manual. Higher PREN resists chloride pitting; the threshold rises with environment severity.
Environment
Minimum PREN
Grade required
Rationale
E1 – E2
≥ 18
SS304 (18.6)
Dry, low chloride; austenitic adequate
E3 – E4
≥ 25
SS316 (25.2)
Molybdenum needed against condensation
E5 – E7
≥ 32
Duplex 2205 (35.0)
Chloride loading exceeds 316 capacity
A PREN shortfall is reported separately from the galvanic couple: the same SS316 flange can be galvanically clean and still be the wrong grade for E6.

## Slide 7
The GC-001 scoring model
Three weighted terms, one composite band
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Score_GC = (0.50 × voltage risk) + (0.30 × area ratio risk) + (0.20 × environment)
Voltage risk 0.50
Normalised potential gap between the coupled materials. The dominant term because it sets whether a cell forms at all.
Area ratio 0.30
Cathode area over anode area. A small anode against a large cathode concentrates current density and perforates fastest.
Environment 0.20
The E1–E7 multiplier. Modifies severity; never creates a finding where no couple exists.
Band
Range
Action
Low
< 0.35
Record only; no BCF issue raised
Medium
0.35 – 0.65
BCF issue, design review
High
0.65 – 0.85
BCF issue, mitigation required
Critical
> 0.85
BCF issue, redesign before fabrication

## Slide 8
How GC-001 reads the IFC model
Inputs, computation and outputs
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
What it queries
IfcPipeSegment, IfcDuctSegment and fittings; material via IfcRelAssociatesMaterial; Pset_PipeSegmentOccurrence for diameter and wall thickness; Pset_CoveringCommon for insulation; spatial containment for environment class; joint adjacency for the couple.
What it computes
Normalises free-text material to a canonical key; resolves the adjacent element at each joint; derives the potential gap; computes cathode-to-anode area ratio from geometry; applies the environment multiplier; produces the weighted composite.
What it writes
A BCF 2.1 topic per finding with viewpoint and camera on the joint; Pset_CorrosionRisk written back to the flagged element carrying mechanism, score, environment class and mitigation; a row in the machine-readable asset register.
Every threshold applied is carried in the versioned ruleset, so a finding can be traced to the clause that produced it.

## Slide 9
Case study 1 — plant room valve assembly
SS316 isolation valve against 304SS flex hose, humid chemical plant
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
20 mV
potential gap SS316 to SS304
4.2 : 1
cathode-to-anode area ratio
E3
humid indoor 1.2× multiplier
0.52
GC-001 composite MEDIUM band
Finding and mitigation
A 20 mV gap is small, but the area ratio concentrates current on the hose. Specify a dielectric union at the transition, or bring both members to a single grade. Design-stage change £2,400 against £18,000 for field replacement with the plant shut down.

## Slide 10
Case study 2 — hospital riser support
Copper pressure tubing bonded to a carbon steel clamp
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
520 mV
potential gap Cu to carbon steel
18 : 1
cathode-to-anode area ratio
E2
heated indoor 1.0× multiplier
0.79
GC-001 composite HIGH band
Finding and mitigation
Copper is strongly cathodic to steel and the clamp is the small anode. Perforation initiates at the clamp contact, inside a wall, above a ward. Specify a plastic-lined clamp or a nylon isolating washer: £800 at design against £6,000-plus for access, replacement and making good.

## Slide 11
Validation approach
What the engine was run against
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
37 / 38
IFC models processed (1 unsupported schema)
8
independent public repositories
116,006
piping elements scored
49,736
MEP elements with resolved geometry
Corpus composition and method
Hospitals, commercial offices, industrial plant and mixed-use models, in IFC2x3 and IFC4, exported from Revit, ArchiCAD and Autodesk toolchains. Each model is downloaded, parsed, scored by every engine and exported to BCF. The one failure is IFC2X2_FINAL, which IfcOpenShell does not support.

## Slide 12
Validation results — what was measured
Engine coverage against real third-party models
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Engine
Elements flagged
Flag rate
Elements with all required inputs
Coverage
GC-001
0 of 116,006
0.0%
8
0.007%
CC-001
116,006 of 116,006
100.0%
0
0.000%
MC-001
116,006 of 116,006
100.0%
0
0.000%
MM-001
unavailable on 24 models
—
15
0.013%
XM-001
unavailable on 24 models
—
0
0.000%
A 0% and two 100% flag rates are properties of input availability, not of the buildings. Where required inputs are absent the coercers substitute a default, so the engine scores the default uniformly. Recorded in thesis §13.9 and Appendix B, Table B.4.
No precision or recall figure is claimed: with coverage below 0.02% there is no population against which either could be computed.

## Slide 13
Performance measured across the corpus
Wall-clock cost of a full sweep
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Metric
Measured value
Note
Total sweep
3,594 s for 37 models
Download, parse, halo, clash, engines, BCF
Mean per model
≈ 97 s
Dominated by geometry evaluation
Largest model
632 s — NBU_MedicalClinic
207 MB multi-discipline archive
Smallest MEP model
4.8 s — wbdg office
31 piping elements
Geometry resolution
49,736 of 49,736 (100%)
ifcopenshell.geom, world coordinates
Bottleneck
Geometry evaluation, then clash
Spatial grid reduces O(n²) pairing
Measured on this corpus, not estimated. Timings are per-model records in validation_sweep_summary.json.

## Slide 14
Academic contribution
What this work adds
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Method, not just result
A documented, reproducible method for interrogating electrochemical risk from IFC metadata alone, with every threshold tied to the standard governing its mechanism. The threshold values are authored calibration, not quoted from those standards.
Quantified data gap
The corpus measures how far real federated models fall short of what a corrosion assessment needs: 38,012 of 116,006 elements carry material text, and only 2,403 normalise to a scoreable key.
White-box auditability
Every finding names the clause, the threshold and the inference that produced it, so a reviewer can disagree with the conclusion on the evidence rather than on trust.
Golden Thread integration
Findings persist into the model as Pset data and into the CDE as BCF topics with ISO 19650 status codes.

## Slide 15
Limitations
Stated plainly
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Binary risk, not current magnitude
The composite ranks risk; it does not compute galvanic current density or metal loss rate. That needs Faraday's law and an electrolyte conductivity model.
Static environment class
One class per element for the model's life. Seasonal humidity swings and commissioning-stage wetting are not represented.
No time-to-failure prediction
The engine does not estimate when perforation occurs; that requires corrosion-rate data beyond the IFC.
Dependent on material specification
Where material is absent or unmappable, the element is reported as a data-quality issue rather than scored. On this corpus that is the majority case.

## Slide 16
Post-FMP roadmap
R1 – R4, with the dependency each carries
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Ref
Enhancement
Dependency
Target
R1
Galvanic current modelling (Faraday's law)
Electrolyte conductivity per environment
Q2 2027
R2
Time-to-perforation calculator
Corrosion-rate dataset, ASTM G48 basis
Q2 2027
R3
Material library expansion beyond 22 entries
Normaliser rule table widening
Q1 2027
R4
BMS integration for live environment class
Sensor feed and IFC round-trip
Q3 2027
R3 is the highest-value item on the measured evidence: 35,609 elements carry material text the normaliser cannot map, so widening the rule table converts unusable text into scoreable input.

## Slide 17
Standards compliance
Standards governing each mechanism; the thresholds are authored calibration
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Standard
Mechanism addressed
Where it is applied
NASA-STD-6012
Galvanic couple voltage thresholds
Voltage risk term, band boundaries
WorldStainless / Euro Inox
Electrochemical series, corrosion data
22-material potential table
IMOA Design Manual
PREN formula and grade selection
PREN adequacy check
AUCSC Basic Corrosion Course
Electrolyte conductivity, area-ratio effect
Area ratio risk term
ISO 16739-1
IFC schema
Element, material and spatial queries
buildingSMART BCF 2.1
Issue exchange format
Topic, viewpoint and snapshot output
All are carried in the versioned ruleset rather than embedded in code, so a threshold change is a reviewable data change.

## Slide 18
Working alongside CC-001
Why two engines, not one combined score
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
They run independently
Each engine evaluates its own mechanism against its own ruleset. Neither can suppress the other's finding.
They emit separate BCF topics
Different mechanisms need different mitigations. A dielectric union does not fix a crevice, and a weld prep does not fix a couple.
Combined band is the higher of the two
Reported for triage only. The underlying findings remain distinct and separately actionable.
Worked example — SS316 flange, pool plant
Galvanically clean at 0.00: a single material, no couple, nothing for GC-001 to see. Crevice band 0.89 Critical: chloride under the gasket face at E7. One element, one engine silent, the other decisive.

## Slide 19
Asset register output
The machine-readable compliance record
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
GlobalId
Material
GC
CC
Combined
Cost £
Days
0NZ34oqSTTyBSJPT5Cw1AX
Copper_C12200
0.79
0.12
HIGH
800
0
1h8Om82ovOQwaLzjgOtw0y
CarbonSteel
0.79
0.34
HIGH
800
0
0CCaRDl7PGav91kwXZIizp
SS316
0.00
0.89
CRITICAL
3,200
4
0ofHWhBlHI7wRekoFS0Xtk
GalvanisedSteel
0.52
0.41
MEDIUM
2,400
2
2aA0fSFYDE6hf08n4QlwRz
SS304
0.18
0.22
LOW
0
0
GlobalIds are real, drawn from the synthetic hospital MEP fixture. Scores are illustrative of the banding, not measured findings — on this corpus GC-001 produced none.

## Slide 20
Pset write-back — creating the Golden Thread
The finding travels with the model, not beside it
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Written to the element
Pset_CorrosionRisk is attached to every flagged element, so the risk is carried by the object rather than by a report that can be separated from it.
What it carries
Mechanism, composite score, risk band, environment class, the governing clause and the recommended mitigation.
Why it persists
It survives export, federation and hand-over between phases, because it is model data rather than an attachment.
Who can audit it
Any IFC-capable reader. No BIMGUARD installation is needed to inspect the evidence under the Building Safety Act.

## Slide 21
ISO 19650 status mapping
How a finding moves through the CDE
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Code
State
Trigger
Exit condition
S2
Work in progress
Any unresolved High or Critical finding
Mitigation applied and re-run clean
S4
Shared for review
Medium findings present; NCR raised
Reviewer accepts or rejects the risk
A
Approved
All engines pass, or residual risk accepted
Released for fabrication
The status code is written into the BCF topic and the CDE container, so the compliance state is visible to the workflow rather than held in the tool.
This is what makes the output an audit trail rather than a report: the state is machine-readable and the transition is recorded.

## Slide 22
RQ1 — answered
Can corrosion risk be detected from IFC data alone?
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
YES
with a material specification present
100%
geometry resolution 49,736 elements
2.07%
elements with a scoreable material
37 / 38
models processed end to end
The qualified answer
The method works: where an element carries a mappable material and a resolvable neighbour, the couple is detected and scored deterministically. The constraint is not the method but the corpus — real federated models rarely carry the inputs. That measurement is itself the contribution, and it is what separates a demonstrated method from a deployed one.

## Slide 23
Key findings
What the corpus established
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
The pairing logic is sound where it can run
Given material on both sides of a joint, the voltage gap, area ratio and environment multiplier produce a deterministic, reviewable band.
PREN adequacy is a separate and useful check
It catches the specification error that galvanic scoring cannot see: the right material, wrongly placed.
Material data, not algorithm, is the limiting factor
38,012 of 116,006 elements carry material text; 2,403 normalise. Widening the normaliser is worth more than refining the score.
OpenBIM held across the corpus
IFC2x3 and IFC4, three authoring toolchains, no vendor API. Same-building schema twins differed by 0.11% and 0.00%.

## Slide 24
Galvanic Corrosion Engine
Questions?
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5