## Slide 1: Two pillars, joined by one rule catalog
Pillar A turns the building code into rules. Pillar B runs those rules on the IFC model. No threshold lives in the software.
PILLAR A · RULE AUTHORING
From code text to a checkable rule
1
Parse the code document
Headings, clauses and tables, each with its page position.
2
Extract draft rules
One draft per clause, with its source and an extraction score.
3
Review by a person
Accept, edit or reject. Conflicts are flagged before promotion.
4
Grade and file
Each rule gets a reliability grade and a check category.
PILLAR B · ARCHITECTURAL AUDIT
From an IFC model to graded findings
1
Match elements to rules
Every element of the rule's IFC class is checked. No sampling.
2
Read the real IFC value
Searched in a fixed order; the source of the value is recorded.
3
Scope, compare, exempt
In scope? Meets the rule? Does a stated exception apply?
4
Give a verdict
One of six outcomes, graded by reliability and confidence.
Rule catalog
database
How rules are categorized
By element type, then by what the rule tests. 48 categories, stored in the database.
12
Windows
Fire and smoke, emergency escape, energy, glazing…
14
Doors
Dimensions, swing, life-safety, clear opening…
22
Stairs and railings
Risers and treads, headroom, guard height…
Notes: Pillar A fills the rule catalog: code documents are parsed, draft rules are extracted, a person reviews every draft, and each accepted rule is graded for reliability and filed under a check category. Pillar B reads from the catalog: every matching element in the IFC model is checked against each rule and given a verdict. Categories: 12 for windows, 14 for doors, 22 for stairs, handrails and guards.

## Slide 2: Every finding: two grades and one verdict
Reliability is known before a model is loaded. Confidence is known once the value has been read. No silent defaults.
Reliability of the rule
If the value is present, is it true?
HIGH
Stored in the file, one source
IFC attribute, element class, stored relationship, Qto quantity
MEDIUM
Standard property set
True when found, but many models do not export it
LOW
Not held in the model
Geometry estimate, custom Pset, manufacturer or user-defined field
A rule takes the grade of its weakest property.
Confidence of the result
Where did this value come from?
Authored property
Derived from model geometry
Type-inherited
Alias match
Rule fallback property
Geometry estimate
Unresolved
Six verdicts
Absent evidence is reported, never assumed
PASS
Value found, meets the rule
FAIL
Value found, breaks the rule
MISSING
Model does not hold the value
NOT ASSESSED
No rule or no evidence
N/A
Outside the rule's scope
UNDETERMINED
Scope cannot be tested
Risk score per finding
Sets the BCF issue priority
LOW
MEDIUM
HIGH
CRITICAL
0
0.35
0.65
0.85
1
Notes: Reliability grades the rule from the IFC property it reads; a rule with several properties takes the weakest grade. Confidence grades the result from where the value was found, shown as a three-bar meter. The six verdicts mean missing evidence is always reported: missing data, an unassessed check, or an untestable scope never becomes a silent pass. The risk score runs from 0 to 1; the default band cut-offs are 0.35, 0.65 and 0.85, and thresholds are read from the rule catalog.