## Slide 1
BIMGUARD AI
Automated OpenBIM Compliance Across Disciplines
OpenBIM · IFC ISO 16739-1 · BCF 2.1 · ISO 19650 · Building Safety Act 2022
Five corrosion engines · One spatial engine · Validated across 37 models from 8 repositories
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5

## Slide 2
The problem BIM cannot currently solve
Corrosion is predictable, preventable, and unchecked
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
3.4%
of global GDP lost to corrosion annually
6–10×
cost multiplier: field versus design-stage fix
0
existing BIM tools that check corrosion in IFC
0 pts
Golden Thread evidence without this work
Clash detection resolves geometry. Two touching elements of incompatible material, or a stainless grade wrong for its environment, produce a clash-free model and a failure in service.
BIMGUARD AI closes that gap using data already present in the model at LOD 300 — no additional modelling effort required.

## Slide 3
Three research questions
The academic scope
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
RQ1 — Detection from existing IFC data
Can corrosion risk in MEP services be reliably identified from material, spatial and zone metadata already present at LOD 300?
RQ2 — Simultaneous multi-mechanism checking
Can several mechanisms be evaluated in one pass, each reporting failures the others cannot see, rather than collapsing into a single score?
RQ3 — OpenBIM cross-platform deployment
Can a checker operating purely on IFC input and BCF output work across authoring tools with no vendor plugin or proprietary API?

## Slide 4
The compliance pipeline
Five stages, each failing independently and saying why
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Stage
Function
Status
1
Geometry normalisation and spatial filter
Implemented, 100% resolution
2
Blue Halo clearance envelope (LOD 350 reservation)
Implemented, validated
3
Corrosion engines: GC-001, CC-001, MC-001, MM-001, XM-001
3 of 5 execute; 2 not wired
4
Resolution hierarchy and mitigation ranking
Designed
5
Reporting: BCF 2.1, Pset write-back, ISO 19650 status
Implemented, 37/37 valid
The architectural ruleset (AR-001 – AR-006) is specified as a sixth family and is not implemented; it is presented separately as design scope.
Stage 3's status is stated in thesis §13.9: the MM-001 and XM-001 packs are approved but not wired into the comparator.

## Slide 5
Engine A — GC-001 galvanic corrosion
Material incompatibility at a joint
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Score = (0.50 × voltage) + (0.30 × area ratio) + (0.20 × environment)
Specified
22-material electrochemical series, 7 environment classes, PREN adequacy for stainless grades. Thresholds from NASA-STD-6012, WorldStainless and IMOA.
Implemented
Executes on all 37 models. Produces bands and writes BCF topics and Pset_CorrosionRisk.
Measured
0 of 116,006 elements flagged. Required inputs present on 8 elements — 0.007% coverage.
The single-element entry point pairs each element with itself, so no couple is ever formed. Recorded as a specification-against-implementation gap.

## Slide 6
Engine B — CC-001 crevice corrosion
Geometry the galvanic check cannot see
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Score = (0.35 × geometry) + (0.40 × CCT margin) + (0.25 × environment)
Specified
Crevice Corrosion Temperature table from SS304 to Titanium Gr 2; 14-type joint geometry library from butt weld to threaded connection — seeded but never executed: every joint scores JT-014 Unknown (Tight).
Implemented
Executes on all 37 models and emits its own BCF topics, independent of GC-001.
Measured
116,006 of 116,006 flagged — 100%. Band floor is Medium; an absent material scores High.
A 100% flag rate with 0% input coverage is the same fact twice: the coercer substitutes a default and the engine scores the default, uniformly.

## Slide 7
Engine C — Blue Halo spatial reservation
The engine the corpus validates cleanly
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
49,736
MEP elements 100% geometry
223,516
clashes detected and exported
37 / 37
BCF archives fully valid
0.00%
schema twin delta
Why this one holds up
Blue Halo depends on geometry, which real exports reliably carry, rather than on semantic property data, which they do not. Every MEP element resolved. Same-building twins in IFC2x3 and IFC4 produced identical and near-identical clash counts, so the result is schema-independent.

## Slide 8
Engines D and E — MM-001 and XM-001
Approved specification, not wired to the comparator
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
What is approved
MM-001 holds a 12-material by 8-media compatibility matrix; XM-001 scores the galvanic couple at a joint between dissimilar modelled elements. Both packs are reviewed at v1.0 with recorded amendments.
What executes
Neither. load_rule_pack() rejects the approved packs because the shipped comparators validate an earlier schema — MM-001 on compatibility_matrix, media, environments and materials; XM-001 on couples, materials and environment_thresholds.
Corroborated independently
The unit suites fail at fixture setup for the same reason: 3 of 29 MM-001 tests and 1 of 39 XM-001 tests execute. The validation sweep and the test suite reached the same conclusion by different routes.
Recorded, not concealed
Thesis §13.9 and Table 13.13 state this term by term: 'no claim in this chapter should be read as asserting' that the wiring exists.

## Slide 9
When mechanisms disagree
Why separate engines rather than one score
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
0.00
GC-001 band no couple exists
0.89
CC-001 band chloride at the gasket
E7
pool plant 1.8× multiplier
CRITICAL
combined band higher of the two
SS316 flange in a pool plant room
A single material, so no galvanic couple and nothing for GC-001 to report. Under the gasket face, chloride concentrates in the crevice at E7 and CC-001 scores it Critical. One element, one engine correctly silent, the other decisive. A single combined score would have averaged the finding away.

## Slide 10
Validation at corpus scale
37 models, 8 repositories, two IFC schemas
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Measure
Result
Note
Models processed
37 of 38
One IFC2X2_FINAL, unsupported by IfcOpenShell
MEP elements
49,736
100% geometry resolution
Structural elements
26,970
26,808 resolved (99.4%)
Clashes detected
223,516
211,581 minor / 6,699 major / 5,236 critical
Piping elements scored
116,006
38,012 carry material text
Scoreable material
2,403 (2.07%)
Normalise to a canonical key
BCF archives valid
37 of 37
Every XML part parsed, every topic complete
Sweep wall-clock 3,594 s, mean 97 s per model.

## Slide 11
Material text is not material data
The measurement that reframes the result
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
116,006
piping elements scored
38,012
carry some material string
2,403
normalise to a scoreable key
2.07%
usable material coverage
The 16× gap
35,609 elements carry material text the normaliser cannot map, so the engines still receive 'Unknown'. Reporting the 32.8% figure as coverage overstates usable data roughly sixteenfold. This distinction is the single easiest way to misread the corpus, and it is why every engine result is published beside its input coverage.

## Slide 12
Standards sensitivity
Clearance choice dominates the outcome
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Clearance
Jurisdiction
Clashes
Critical
Ratio
25 mm
—
30,332
148
0.29×
100 mm
—
69,307
38
0.67×
200 mm
SB-001 authored calibration¹
104,144
31
1.00×
457.2 mm
—
172,812
16
1.66×
600 mm
—
212,870
11
2.04×
¹ BIMGUARD SB-001 screening calibration (authored thresholds, not code values)
Raising the clearance from the 200 mm row to the 457.2 mm row produces 66% more clashes and 48% fewer Critical ones, because severity is an overlap ratio and a larger clearance inflates the denominator. Reproduced on two independent subsets.

## Slide 13
Test evidence
What runs, and what the failures mean
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Suite
Result
Interpretation
Core suite (tests/)
289 passed
Piping, comparators, BCF, registry, environment
Route suite (tests/test_routes.py)
44 passed, 4 xfail
HTTP layer; xfail records 404-vs-200 gaps
Blue Halo harness
11 of 11
Config, geometry, clash, banding, export
End-to-end IFC pipeline
8 of 8
Real IFC through halo, clash, BCF, Pset
MM-001 / XM-001 suites
69 failures / errors
Signature mismatch — corroborates §13.9
The 69 failures are not noise to be silenced: they are executable evidence for the specification-against-implementation gap the thesis documents, which is why §13.9 can quote exact pass counts.

## Slide 14
Technology stack
Deliberately vendor-neutral
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Core
Python 3.12.13, IfcOpenShell 0.8.5, uv-managed dependencies. Geometry through ifcopenshell.geom in world coordinates.
Application
FastHTML with MonsterUI, HTMX for partial updates, server-rendered from Python — no template files.
Data
Supabase Postgres and object storage, with a transparent local materialisation cache.
Analytics
Power BI PBIP project — TMDL semantic model plus report definition, consuming a versioned CSV contract.
No Autodesk API, no proprietary plugin, no authoring-tool dependency anywhere in the compliance path.

## Slide 15
OpenBIM as an architectural decision
Why vendor neutrality was not incidental
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
IFC in, BCF out
The tool reads ISO 16739-1 and writes BCF 2.1. Both are open, versioned and readable without the tool that produced them.
Demonstrated across toolchains
The corpus spans Revit, ArchiCAD and Autodesk exports in IFC2x3 and IFC4. Schema twins differed by 0.11% and 0.00%.
Evidence outlives the tool
Pset write-back means the finding travels in the model. An auditor needs an IFC reader, not a BIMGUARD licence.
Portable across jurisdictions
Clearance and threshold data live in versioned configs, so a new standard is a data addition rather than a code change.

## Slide 16
Golden Thread and the Building Safety Act
Compliance evidence that persists
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Requirement
How it is met
Artefact
Auditable decision record
Every finding names clause, threshold and inference
BCF topic + Issue citations
Evidence travels with the asset
Findings written back to the element
Pset_CorrosionRisk, Pset_HaloReservation
Readable without the tool
Open formats throughout
IFC, BCF 2.1
Traceable workflow state
ISO 19650 status on each container
S2 / S4 / Status A
Reproducible
Harness, configs and corpus are versioned
Appendix B, validation_sweep_summary.json
Reproducibility is the claim most examiners can check directly: the sweep re-runs from a clean clone and regenerates every table and figure in Appendix B.

## Slide 17
RQ1 — answered
Detection from existing IFC data
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
YES
method demonstrated and reproducible
100%
geometry resolution 49,736 elements
2.07%
elements carrying scoreable material
37 / 38
models processed end to end
The qualified answer
Where an element carries a mappable material and a resolvable neighbour, risk is detected and scored deterministically from data already in the model. The constraint is the corpus, not the method: real federated models rarely carry the semantic inputs. Measuring that distance is itself a contribution, and it separates a demonstrated method from a deployed one.

## Slide 18
RQ2 — answered
Simultaneous multi-mechanism checking
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Architecturally — yes
Engines register independently, share one mechanism-agnostic Issue contract, and emit separate BCF topics. Three execute together on every model in the corpus.
Demonstrated by non-overlap
The SS316 pool-plant case shows one engine correctly silent while another reports Critical — the behaviour a single combined score would destroy.
Two of five do not participate
MM-001 and XM-001 are approved but unwired, so the full five-mechanism claim is not supported by this run.
Honest form of the answer
Simultaneous checking works and is demonstrated at three engines. Five is specified, not shown.

## Slide 19
RQ3 — answered
OpenBIM cross-platform deployment
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
YES
no vendor API anywhere in the path
2
IFC schemas 2x3 and IFC4
8
independent source repositories
37 / 37
BCF archives valid
What the corpus established
Models exported from three authoring toolchains, in two schema versions, from eight repositories, processed by one pipeline with no per-tool special-casing. The two same-building schema twins are the strongest control: identical inputs through different exporters produced clash counts 0.00% and 0.11% apart.

## Slide 20
Academic contributions
Five, stated at the level the evidence supports
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Contribution
Evidence
A reproducible method for corrosion assessment from IFC metadata
37-model sweep, regenerable from a clean clone
Quantification of the semantic data gap in federated models
2.07% scoreable material across 116,006 elements
Blue Halo: proactive LOD 350 reservation at LOD 300
100% geometry resolution, schema-independent
White-box auditability as a design constraint
Every finding carries clause, threshold and inference
A clearance-severity inversion in ratio-based banding
1.66× clashes, 0.52× Critical, on two subsets
Each is stated as what was measured, not as what was hoped. The gaps — two unwired engines, an unimplemented ARCH ruleset — are documented in §13.9 rather than omitted.

## Slide 21
Limitations
Carried openly
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Two engines are not wired in
MM-001 and XM-001 hold approved packs the comparators cannot load. 69 unit failures and 24 unavailable models corroborate the same gap.
Input availability limits every corrosion result
At 2.07% scoreable material, flag rates describe the coercers' defaults more than the buildings.
Clash counts are geometric upper bounds
AABB intersection over-approximates diagonal and non-convex members.
Severity banding lacks a standards basis
An overlap ratio is defensible as triage and not as a verdict; the sensitivity result argues for replacing it.

## Slide 22
Post-FMP roadmap
Seven enhancements, ordered by dependency
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Ref
Enhancement
Why it ranks here
Target
R1
Wire MM-001 and XM-001 to the approved packs
Closes the largest documented gap
Q1 2027
R2
Widen the material normaliser rule table
Converts 35,609 unusable strings into input
Q1 2027
R3
Standards-grounded severity model
Replaces the ratio heuristic
Q2 2027
R4
Angle-aware halo envelope
Needs brace geometry to validate
Q2 2027
R5
Implement ARCH rules AR-001 and AR-004
Extends method to code compliance
Q2 2027
R6
Galvanic current and time-to-perforation
Needs conductivity and rate data
Q3 2027
R7
Labelled validation corpus
Prerequisite for any accuracy claim
Q3 2027
R2 is the highest measured value for the least effort: the corpus already quantifies exactly how much input it would unlock.

## Slide 23
What the corpus established
Findings across all engines
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5
Geometry generalises; semantics do not
100% geometry resolution against 2.07% scoreable material. The spatial engine works on real models; the corrosion engines are starved of input.
Independent engines catch independent failures
The pool-plant case is the proof: one engine silent, another Critical, on the same element.
The result is schema-independent
Two IFC versions, three toolchains, eight repositories, one pipeline — twins 0.00% and 0.11% apart.
Reporting coverage beside findings is essential
Without it, a 100% flag rate reads as a result rather than as an artefact of absent data.

## Slide 24
BIMGUARD AI
Questions?
BIMGUARD AI | Final Master Project | Zigurat Global Institute of Technology | Group 5